## Slide 1: Packet Number Space(s)
Christian Huitema
October 18, 2021
Why two options for numbering packets?

## Slide 2: Numbering packets
Two options
  Single number space (draft-huitema)
  One number space for each path (draft-liu, draft-deconinck)
There are pros and cons in each approach

## Slide 3: Single Number Space
Packets are numbered in sequence, as they are sent
Same as QUIC V1
Same ACK format as QUIC V1
Sender keeps track of which packet went on what path
Out of sequence delivery common if paths have different latencies
1
2
4
3
6
5

## Slide 4: Multiple Number Space
On packet sequence per path
Sender maintains separate list of packets waiting for acknowledgements per path
New “per path” acknowledgement frame
Requires changes in packet encryption/decryption
1
2
3
1
3
2

## Slide 5: Encryption-decryption issue (Multiple spaces)
Default behavior:
  AEAD Nonce = IV + 64 bit packet number
But same PN on multiple path means same nonce
  Not compatible with AEAD, same nonce means same encryption
Solution: 96 bit AEAD nonce
  AEAD Nonce = IV + (32 bit CID sequence number | 64 bit packet number)
  Supported by several TLS stacks
Not possible if using NULL CID
ENCRYPTED PAYLOAD
1
rtt
CID
PN

## Slide 6: ACK Ranges issue (single space)
Paths with different latencies
  Out of order deliveries
  Large number of ACK ranges
  Case of CWIN = 10,000 packets?
Mitigate requires smarts
  Send in batches (GSO)
  Limit number of ranges in ACK
  Limit number of ACK per range
  ACK horizon
  ACK of ACK
1
2
4
3
6
5
ACK 8, 5-6, 3, 1
8
7

## Slide 7: Loss recovery issue (single space)
RFC 9002 specifies RACK
  Assumes approximate in order delivery
  Multipath breaks that
Mitigation
  Remember send path of packet
  Perform RACK logic “within a single path”
1
2
4
3
6
5
ACK 8, 5-6, 3, 1
8
7

## Slide 8: Pros and cons
Single space
Support for NULL CID
  Minimal transmission overhead
Fewer code changes
  Lots of code assumes single packet number space
Does not require 96 bit nonce
  Fewer crypto stack requirements
Allows implementation trade-offs
  Complexity vs efficiency
Multiple spaces
No worries about ACK ranges
  Works well, even if large CWIN
Simple logic
  Per path version of RFC 9002 algorithms
Does not require implementation trade-offs

## Slide 9: Decision so far: just specify both options
Allow for negotiation during handshake
  Chose one, or other, or none.